| Police Department Safety Checklist Minimum Frequency Quarterly |
| --- |
| Municipality: | Inspection Date: / / 201__ |
| Name of Inspector: | Title: |
| Location Surveyed: |
| # | Needs Work | OK | N/A | CONDITION: Write line #’s & comments on back for all “Needs Work” listings, and notify management to initiate required corrective action |
|  | Building Conditions |
| 1 |  |  |  | Stairs clear & handrails secure, stair treads in good repair? Y N |
| 2 |  |  |  | Exits identified, emergency lights function, occupancy posted |
| 3 |  |  |  | All transaction windows protected & duress alarms? Alarms tested annually? Y N |
| 4 |  |  |  | Fire doors kept closed, latches & automatic closures work |
| 5 |  |  |  | Floors & aisles clean; slip, trip & fall hazards eliminated |
| 6 |  |  |  | Interior lighting adequate? Check coverage of Emergency Lighting |
| 7 |  |  |  | Grounds & walkways in good condition; Exterior lighting adequate |
|  | Building, Housekeeping & Sanitary Conditions |
| 8 |  |  |  | Offices clean, adequate walking area, smooth floor, no hazardous chemicals |
| 9 |  |  |  | Basement, clear access, adequate headroom, lighting |
| 10 |  |  |  | Electrical/heater room, pressure relief piped to floor |
| 11 |  |  |  | Records storage, evidence lockers & ammunition secured. |
| 12 |  |  |  | Lockers secured, no moisture damage, shower facilities provided |
|  | Power Sources |
| 17 |  |  |  | Computers & radio equipment provided with surge protection? |
| 18 |  |  |  | Emergency lighting operational |
| 19 |  |  |  | 36 inches clearance in front of electrical panels? Arc-flash labeling in place? |
| 20 |  |  |  | GFCI’s where needed within 6 foot of sinks? |
| 21 |  |  |  | Emergency generator exercised weekly, tested under load & log maintained? |
|  | Vehicle Fueling □ No fueling done at this location: skip lines 23-25 |
| 23 |  |  |  | Fuel tanks are labeled with name, CAS # & NFPA Hazard codes? |
| 24 |  |  |  | Minimum of a 20 BC rated extinguisher is within 50 feet of tank? |
| 25 |  |  |  | NO SMOKING signs posted, emergency fuel shut-off identified? |
|  | Fitness Area □ No fitness center skip lines 26 & 27 |
| 26 |  |  |  | Usage rules for equipment posted |
| 27 |  |  |  | Equipment visually inspected for defects |
|  | Dispatch Area □ No dispatch operation at this location: Skip lines 28 & 29 |
| 28 |  |  |  | Access to room is restricted to authorized people? Workstation Ergonomic issues? |
| 29 |  |  |  | Power cords & cables properly secured |
|  | Fire Detection / Suppression □ No sprinklers; skip lines 30-32 |
| 30 |  |  |  | Fire alarm and/or detection system, functional, inspected annually Y N |
| 31 |  |  |  | Fire suppression (sprinklers) system, functional, inspected annually |
| 32 |  |  |  | Fire extinguisher serviced annually & inspected monthly |

| Line # | Comments or action taken |
| --- | --- |

Space for drawings or sketches if needed to explain comments: