| Special Equipment Checklist – Bulk Propane Suggested frequency minimum once per year |
| --- |
| Municipality | Inspection Date: / /20 |
| Name of Inspector: | Title: |
| Location Surveyed: | Tank capacity: WC = gallons |
| Reference: Chapter 8 of the Liquefied Petroleum Gas Code, NFPA 8-2014 |

If own more than one, each is uniquely identified, Use separate sheet for each tank

| # | Needs work | OK | N/A | Item Write line # & comments on back for each needs work item |
| --- | --- | --- | --- | --- |

Propane Tanks   Municipality does not own this equipment □

|  |  |  |  | Do you have a copy of N.J.A.C. 5:18-1.3? revised June 19, 2017 |
| --- | --- | --- | --- | --- |
|  |  |  |  | Tanks > 1,000 gal WC must be registered with the state! Is it? |
|  |  |  |  | Is the manufacturer’s name plate in place and legible? |
|  |  |  |  | Tanks exceeding 250 gallons WC shall be provided with a marker plate indicating who should be called in the event of an emergency involving the LP-Gas container |
|  |  |  |  | Tank has “Propane” on the tank in at least 4” high letters? |
|  |  |  |  | Tank has the CAS # 74-98-6 on the side of the tank |
|  |  |  |  | Tank has a prominent “No Smoking” sign posted? |
|  |  |  |  | Date of last inspection of the Pressure relief valve? / / |
|  |  |  |  | Is the tank level on its pad or cradle? |
|  |  |  |  | Tank secured to the ground? Unsecured tanks can float in a flood. |
|  |  |  |  | Is the tanks paint in good condition? |
|  |  |  |  | Tank is painted white or a light reflecting color? Dark is prohibited |
|  |  |  |  | Combustible weeds & tall grass closer than 10‘from tank? |
|  |  |  |  | Is there at least 25’ between this tank and any other structure? |
|  |  |  |  | Physical protection around the tank is provided by bollards? |
|  |  |  |  | Posts must be a minimum of 4” schedule 40 pipe & painted yellow. |
|  |  |  |  | Posts are to be set at 4 feet 6 inches maximum centers. |
|  |  |  |  | Visually inspect for damage, gouges and severe rust? |
|  |  |  |  | Is the “Yard line” from tank to appliance buried or shielded? |
|  |  |  |  | Lock-in-Place dome provided to prevent unauthorized use? |
|  |  |  |  | Visually look for debris in the relief valve, there should not be any? |
|  |  |  |  | Has tank been hydrostatically tested within 12 years? |
|  |  |  |  | Does this tank have capacity greater than 4000 gallons? Y N |
|  |  |  |  | If answer above is yes complete the following |
|  |  |  |  | Does your tank contain an “excess flow” check valve? |
|  |  |  |  | Does your tank contain an “emergency shut-off” valve? |
|  |  |  |  | Is any water spray fire suppression in place around your tank? |
|  |  |  |  | Is the fire department aware of this tank? Y N |
| N |  |  |  |  |